## Slide 1
QKD Simulation Framework — 40-Minute Presentation Deck
A Unified Simulation Framework for Discrete-Variable Quantum Key Distribution
Presenter: Reza Aramjou
Date: August 2026
Duration: 40 minutes (18 slides × ~2 min + buffer)

## Slide 2
SLIDE 1
1
A Comprehensive QKD Simulation Framework — Bridging Quantum Theory and Software Engineering
A Unified Simulation Framework for Discrete-Variable Quantum Key Distribution
From Optical Pulse Generation to Composable Security Proofs and Network Routing
Reza Aramjou — August 2026
🎤 Good morning, everyone. Thank you for being here. Today I'm going to present a comprehensive simulation framework for Quantum Key Distribution — or QKD — that I have developed over the past several months. This is not merely a key-rate calculator. It is a full-stack research infrastructure that models the entire pipeline from the generation of individual optical pulses, through the physics of fibe…

## Slide 3
SLIDE 2
2
Motivation — Why QKD Matters Now
Classical public-key cryptography relies on computational hardness (factoring, discrete log)
Shor's algorithm breaks RSA/ECC in polynomial time on a fault-tolerant quantum computer
"Harvest Now, Decrypt Later": data intercepted today can be decrypted tomorrow
QKD offers information-theoretic security based on the laws of quantum mechanics
Complementary to Post-Quantum Cryptography; QKD + PQC coexist in hybrid architectures
🎤 Let me set the stage. The security of virtually all deployed public-key cryptography — RSA, elliptic-curve cryptography — rests on the computational difficulty of factoring large integers or solving discrete logarithms. These are problems that a sufficiently powerful fault-tolerant quantum computer, running Shor's algorithm, can solve in polynomial time. The threat is not merely theoretical. There…

## Slide 4
SLIDE 3
3
Bridging the Theory–Engineering Divide
Most tools oversimplify physics or hard-code a single security proof
Real-world effects neglected: dead-time cascades, afterpulsing, DWDM cross-talk
Asymptotic analyses ignore finite-key statistics — essential for practical systems
This framework unifies: rigorous physics + multiple composable proofs + network orchestration
Design principles: layer separation, immutability, fail-fast validation, single source of truth
🎤 There is a substantial gap between how QKD is described in theoretical papers and what is needed to build a trustworthy simulation. Most published protocols derive asymptotic key-rate formulas under idealized assumptions: perfect single-photon sources, detectors with no dead time, infinite pulses. Many existing simulation tools compound the problem by hard-coding a single security proof and using …

## Slide 5
SLIDE 4
4
System Architecture — A Layered, Modular Design
Physical Layer: Coherent/thermal sources, SNSPD/SPD/PNRD detectors, FiberChannel with Beer-Lambert, noise models
Cryptographic Layer: FiniteKeyProof ABC, four proofs, epsilon-budget allocation, LP parameter optimization
Execution Layer: Parallel workers, log/linear sweeps, auto-optimization via SLSQP, CSV output
Network Layer: 7-node trusted-relay topology, 10 links, 20 key pools, SPF+ routing, failover
🎤 Let me walk you through the four-layer architecture. At the bottom is the Physical Layer, implemented in the qkd Python package — optical source models, detector models including SPD, SNSPD, and PNRD with dead-time and afterpulsing, and the fiber channel with Beer-Lambert attenuation and noise models. Above that sits the Cryptographic Layer, centered on the FiniteKeyProof abstract base class. Ever…

## Slide 6
SLIDE 5
5
QKDParams — Centralized, Immutable, Validated Configuration
QKDParams is the single entry point (~1,700 lines, type-driven)
Deep validation of 50+ parameters at construction (fail-fast)
Immutable: @dataclass(frozen=True) — no accidental mutation
Schema versioning (v1.9) ensures cross-version reproducibility
Factory presets reproduce published Lim 2014 benchmarks
Serialization: to_serializable_dict() ↔ from_dict()
🎤 A key architectural decision is the centralization of all configuration into a single, immutable, deeply validated data structure called QKDParams — a frozen Python dataclass over 1,700 lines. When constructed, the _validate() method runs over fifty checks. If any fails, construction raises an explicit exception immediately — fail-fast. The object is frozen after construction. If you need a modifi…

## Slide 7
SLIDE 6
6
FiberChannel — Immutable Physics with Numerical Safeguards
Core: T = 10^(−αL/10), α ≈ 0.2 dB/km at 1550 nm
All channel objects immutable — frozen dataclass
Numerical safeguards: subnormal clamping, safe_log, underflow detection
Strict mode: warnings → hard exceptions for production
ElectricalNoiseConfig: Johnson-Nyquist + Schottky shot noise
DWDM nonlinear cross-talk for multi-channel
🎤 The fundamental channel model is Beer-Lambert: transmittance T equals ten to the power of negative alpha-L over ten, with alpha approximately 0.2 dB/km at 1550 nm. For long distances beyond 300-400 km, transmittance becomes astronomically small — below IEEE-754 subnormal thresholds — and can underflow to zero, silently corrupting entropy calculations. The framework detects these conditions and app…

## Slide 8
SLIDE 7
7
Optical Sources and Detector Models
Coherent Source: Poisson photon statistics, configurable μ per pulse
Decoy-state: signal (μ ≈ 0.4–0.8), decoy (ν ≈ 0.1–0.2), vacuum
SPD: η ~0.15–0.3, Y₀ ~10⁻⁶/gate, moderate cost
SNSPD: η ~0.5–0.9, Y₀ ~10⁻⁸/gate, cryogenic, best long-distance
PNRD: photon-number-resolving for advanced protocols
All detectors: configurable dead-time models and afterpulsing
🎤 The framework models coherent laser sources with Poisson-distributed photon numbers. For the decoy-state protocol — critical for defeating photon-number-splitting attacks — the source emits at signal, decoy, and vacuum intensities. On the detector side: SPDs with efficiencies around 15-30% and dark counts around 10⁻⁶ per gate; SNSPDs with 50-90% efficiency and dark counts as low as 10⁻⁸ per gate b…

## Slide 9
SLIDE 8
8
Protocol Pipeline — From Pulses to Sifted Keys
BB84: Alice prepares Z/X basis; Bob measures randomly
Basis sifting discards ~50% of detections via classical channel
Decoy-state: estimates Y₁ (single-photon yield) and e₁ (error) from intensity statistics
Tally counts by (basis, intensity) pair feed security proofs
ProtocolParameters dataclass provides uniform abstraction
🎤 In the BB84 protocol with decoy states, Alice randomly selects a basis and intensity level each round. Bob independently chooses a measurement basis. After quantum transmission, basis sifting discards mismatched-basis rounds — roughly half. The remaining events are sorted into tally categories by basis and intensity. These tally counts drive the decoy-state analysis: because Eve cannot distinguish…

## Slide 10
SLIDE 9
9
FiniteKeyProof — The Abstract Security Framework
All proofs inherit from FiniteKeyProof ABC — uniform interface, comparable outputs
Template Method: compute_key_rate() orchestrates ε-allocation → yield estimation → key-length
Epsilon decomposition: ε_sec divided among error correction, privacy amplification, parameter estimation
TallyCounts: raw (basis, intensity) counts
DecoyEstimates: Y₁^L, e₁^U, feasibility flag
KeyCalculationResult: final secure key length, leak breakdown, diagnostics
🎤 All security proofs inherit from a single abstract base class called FiniteKeyProof. This enforces a uniform interface — every proof exposes the same methods and produces the same output data structures, which is essential for fair cross-proof comparisons. The base follows the Template Method pattern. compute_key_rate orchestrates: allocate_epsilons decomposes the total security parameter into sub…

## Slide 11
SLIDE 10
10
Proof Comparison — Lim 2014, Ma/Wang, and Tight Proof
Lim 2014: Dedicated + DWDM presets, optimized for realistic fiber
Ma 2005: Foundational decoy-state proof, rigorous Y₁/e₁ framework
Wang 2005: Alternative statistical bounding, different variance treatment
Tight Proof: Asymptotically optimal rates, minimal ε-leakage overhead
All proofs use the same physical simulation engine
Differences attributable solely to cryptographic assumptions
🎤 The framework implements four concrete security proofs. The Lim 2014 proof handles both dedicated-fiber and DWDM scenarios with finite-key corrections and factory presets. The Ma 2005 proof provides the foundational decoy-state security analysis. The Wang 2005 proof offers an alternative statistical treatment. The Tight proof achieves rates approaching the asymptotic optimum by minimizing epsilon-…

## Slide 12
SLIDE 11
11
Linear Programming — Optimizing Protocol Parameters
LP formulation: maximize key rate subject to decoy-state + physical constraints
SLSQP solver (scipy.optimize.minimize) for non-linear extensions
Campaign 4: auto-optimization finds optimal μ, ν, probabilities per distance
Constraints: Y₁ ≥ 0, e₁ ≤ 0.5, μ > ν > 0, Σp = 1.0
Result: ~15–25% key rate improvement over manual parameters at intermediate distances
🎤 One of the most powerful features is integrated parameter optimization. Given a fixed fiber length and detector, what combination of intensities maximizes the secure key rate? We formulate this as constrained optimization with SLSQP. The decision variables are source intensities and their probabilities. Constraints come from decoy-state analysis and physical limits. Campaign 4 is dedicated to auto…

## Slide 13
SLIDE 12
12
Network Layer — Trusted-Relay QKD at Metropolitan Scale
7 nodes: 4 senders, 2 trusted relays, 1 receiver
10 fiber links, 20 independent key pools (2 per link)
Trusted Relay: key hops through intermediate nodes; relays must be physically secured
Two backends: full pipeline (PipelineQKDLinkSimulator) + analytical fallback
Key pools: LOW watermark triggers replenishment, HIGH stops
Periodic background replenishment keeps all pools healthy
🎤 Scaling up to a full network: a 7-node metropolitan-scale trusted-relay architecture. Four senders — D through G — connect through two relays — B and C — to receiver A, with ten fiber links and twenty key pools. The trusted relay model is the standard practical approach for extending QKD range. Each relay decrypts and re-encrypts key material, so relays must be physically secured. Each key pool ha…

## Slide 14
SLIDE 13
13
SPF+ — Shortest-Path-First with Key-Pool Awareness
SPF+ extends Dijkstra with dynamic link costs based on key-pool fill ratio
Link cost = base metric + penalty ∝ 1/(fill ratio)
Depleted pools → cost = ∞ → link excluded
Automatic failover: DOWN link → immediate SPF+ recalculation
Complexity: O((V+E) log V) ≈ 50 ops per request — negligible
Demo: B-D failure → D-A reroutes via C, then recovery
🎤 SPF+ extends Dijkstra with dynamic costs based on key-pool availability. When a pool is full, cost equals base metric. As it drains, a penalty inversely proportional to fill ratio increases cost. Below CRITICAL watermark, cost becomes infinity, removing the link. This provides automatic load balancing and failover. In the demo, link B-D fails — D-to-A requests automatically reroute through C. Afte…

## Slide 15
SLIDE 14
14
Validation Strategy — Physics Benchmarks and Cryptographic Checks
Physical invariants: monotonicity, round-trip symmetry, noise additivity
Beer-Lambert validated 0–500 km, relative error < 10⁻¹²
Rogers et al. benchmark: reproduced published key-rate curves (Campaign 9)
Epsilon self-consistency: Σ ε_i ≤ ε_sec for all proofs
Y₁/e₁ estimates verified against analytical asymptotic bounds
50+ parameter checks in QKDParams._validate()
🎤 Validation is built into every layer. Physical invariants: transmittance must decrease monotonically, round-trip must recover original transmittance, noise variances must add linearly. Beer-Lambert implementation validated against closed form across 0–500 km with relative errors below 10⁻¹². Cryptographic validation: Campaign 9 reproduces the Rogers et al. reference curves for decoy-state BB84 — o…

## Slide 16
SLIDE 15
15
Software Validation — Concurrency and LP Solver Integrity
Worker isolation: sub-counts sum to single-worker total
Deterministic reproducibility: fixed seed → bit-identical CSV with 1/2/4/8 workers
Key-pool atomicity: concurrent ops maintain total key count invariant
LP solver: 20+ test cases — simple, degenerate, decoy-state
Failure injection: infeasible, unbounded, ill-conditioned → graceful diagnostics
SolverDiagnostics dataclass captures status, iterations, violations
🎤 Beyond physics and cryptography, the framework undergoes rigorous software validation. Concurrency tests verify worker isolation, deterministic reproducibility with fixed seeds regardless of worker count, and key-pool atomicity under concurrent access. The LP solver is validated against over twenty test cases — simple problems with known optima, decoy-state estimation problems, degenerate cases, a…

## Slide 17
SLIDE 16
16
Ten Campaigns, ~1,800 Simulation Points
C1: BB84+Lim2014 baseline — 96 pts (distance sweep)
C2: Finite-key scaling — 288 pts (pulses 10⁴→10⁸ × distance)
C3: DWDM multi-channel — 288 pts (power −20/−34/−40 dBm)
C4: Auto-optimized (SLSQP) — 96 pts
C5: 4-protocol comparison — 384 pts
C6: 4-proof comparison — 384 pts
C7: 3-detector comparison — 288 pts
C8: Confidence-bound comparison — 288 pts
C9: Rogers et al. validation — 96 pts
C10: Sensitivity (QBER × misalignment) grid
🎤 The framework was exercised through ten distinct simulation campaigns totaling approximately 1,800 points. Each point is a complete run: pulse generation, channel transmission, realistic detection, basis sifting, statistical parameter estimation, decoy-state LP, and finite-key security proof. Campaigns 1-4 cover baselines, scaling, DWDM, and optimization. Campaigns 5-8 perform controlled compariso…

## Slide 18
SLIDE 17
17
Key Findings — What the Simulations Tell Us
Detectors: SNSPD doubles secure range vs SPD; PNRD for advanced protocols
Protocols: Decoy-state BB84 outperforms non-decoy variants
Proofs: Tight proof yields ~10–15% higher rate than Lim 2014; Ma/Wang intermediate
Confidence: Clopper-Pearson most conservative; Gaussian maximizes rate for large N
Sensitivity: 0.01 rad misalignment → 50% key rate reduction
Optimization: SLSQP-optimized intensities → 15–25% improvement at intermediate distances
🎤 Key findings. Detectors: SNSPDs double the secure distance versus SPDs, primarily due to thousand-fold lower dark counts. Proofs: the Tight proof achieves 10-15% higher key rates than Lim 2014 at equivalent security — tighter statistical bounds directly translate to performance. Confidence methods: Clopper-Pearson is most conservative; Gaussian maximizes rates for large N. For N below 10⁵, Clopper…

## Slide 19
SLIDE 18
18
Summary and Outlook
Framework: Complete DV-QKD infrastructure — 4 layers, 4 proofs, 3 detector types, 7-node network
Engineering: Immutable config, fail-fast validation, composable contracts, deterministic reproducibility
Validation: Physics benchmarks, crypto cross-checks, Rogers reproduction, concurrency correctness
Key Insight: SNSPD + Tight proof + optimized intensities = best practical performance
Future: MDI-QKD, quantum repeaters, real-time KMS, ML optimization, CV-QKD extension
🎤 Let me conclude. I have presented a comprehensive DV-QKD simulation framework spanning four architectural layers, four composable security proofs, three detector types with realistic imperfections, and a 7-node trusted-relay network with key-pool-aware routing. The framework is engineered with production scientific software rigor. The key practical insight: combine SNSPD detectors with the Tight s…